## Slide 1: Embedded MP3 Player
Brady Thornton & Jason Brown (Group 12)
Notes: “Introduce group members and any parts of the project each has lead”

## Slide 2: Motivation
  Practical and appealing to technical and non-technical individuals alike
  Well-defined subject matter with a clear end goal
  Interesting design challenges with streaming data and state machines

## Slide 3: Functionality
  Browsing and selecting MP3 files on the SD card via pushbuttons and LCD screen
  Decoding and playing MP3s to the audio out jack
  Equalization of music automatically based on genre in ID3 tag
  Feature-rich web interface for controlling the player remotely
    Customizable multiband graphic equalizer
    Album art and artist info using third-party web APIs

## Slide 4: Functionality Extensions (Time Permitting)
  Touchscreen interface
  Network audio streaming over Ethernet
  Media centre-like library management
    Upload new MP3 tracks via web interface
    Create and organize playlists
    Fill missing ID3 tag data from a web API

## Slide 5: Project Management
  Brady
    MP3 decoding, buffering, and metadata gathering
    Media hardware interfaces (SD card, audio codec)
    Web user interface implementation
  Jason
    Player state machine design and implementation
    Internal and external APIs for player control
    Web server hardware interface

## Slide 6: Hardware
Leverages built-in Altera DE2 components with some interfacing glue in the FPGA
Use of open IP cores wherever possible (SD IP core, audio codec)
Communication between blocks occurs on the Avalon bus
System Boundary
NIOS II CPU
SDRAM
Audio Codec
LCD
SD Card Reader
Push Buttons
Avalon Bus
I2C Bus
SD Card
With MP3 Data
Audio Out (Headphone Jack)
Out
In
InOut
Ethernet Controller
Ethernet Port

## Slide 7: Software Organization
The “Mp3Player” class exposes a public static API to allow different endpoints to make requests (e.g., main LCD/buttons UI, web interface)
State dependent API requests are serviced by the current state representation of the system in a finite state machine architecture

## Slide 8: State Machine Representation

## Slide 9: Decoding MP3s
MP3 decoding and equalization will be done in software
Input and output to the decoder will be buffered
One of two open-source MP3 decoding libraries will be used; libmpg123 or libmad
Selection of library will be based on relative performance in the FPGA
Read bytes from SD card
Input buffer bytes to MP3 decoding library
Equalize decoded PCM samples
Output buffer PCM samples to codec
While !EOF

## Slide 10: Design Challenges
  MP3 decoding
    Implementation of decoding library APIs in desktop simulations
    Verifying correctness of decoded PCM samples prior to implementing the audio core in the DE2
    Evaluating different library implementations for performance, ease of use, and feature sets

## Slide 11: Code Example
Finite State Machine Unit Testing

## Slide 12
// Finite State Machine Controller Class
class StateController
{
public:
StateController(State* initialState);
~StateController();
// Register states and map exit codes to next state
void RegisterState(State* instance,
std::map<int, State*> transitions);
void StartController();
void Update(control_code code);
private:
void TransitionState(int updateCode);
State* _currentState;
bool _running;
std::vector<State*> _states;
std::map<State*, std::map<int, State*>> _stateTransitions;
};
// State Interface
class State
{
public:
virtual ~State(){};
virtual void OnEnter() = 0;
virtual void OnExit () = 0;
virtual int Update (control_code code) = 0;
};

## Slide 13
// State machine test case
_TEST_CASE(StateControllerTest)
{
class MockState : public State
{
public:
virtual void OnEnter() { _lastMsg = _name + " : OnEnter()";
*_output = &_lastMsg; }
virtual void OnExit () { _lastMsg = _name + " : OnExit ()";
*_output = &_lastMsg; }
virtual int Update (control_code code)
{
stringstream ss;
ss << _name << " : update code " << code;
_lastMsg = ss.str();
*_output = &_lastMsg;
return code;
}
MockState(const string &stateName, string **output)
: _name(stateName), _output(output){};
private:
string _name;
string _lastMsg;
string **_output;
};
string *stateOutput = &string();
MockState StateOne = MockState("StateOne", &stateOutput);
MockState StateTwo = MockState("StateTwo", &stateOutput);
StateController controller = StateController(&StateOne);
// Set up state transitions
map<int, State*> transitionsOne, transitionsTwo;
transitionsOne[1] = &StateOne;
transitionsOne[2] = &StateTwo;
transitionsTwo[1] = &StateOne;
// Register the transitions with the controller
controller.RegisterState(&StateOne, transitionsOne);
controller.RegisterState(&StateTwo, transitionsTwo);
// Started in StateOne?
controller.StartController();
_TEST_ASSERT(stateOutput->compare("StateOne : OnEnter()") == 0, 1);
// StateOne update and transition back to self
controller.Update((control_code) 1);
_TEST_ASSERT(stateOutput->compare("StateOne : update code 1") == 0, 2);
// StateOne update and transition to StateTwo
controller.Update((control_code) 2);
_TEST_ASSERT(stateOutput->compare("StateTwo : OnEnter()") == 0, 3);
return 0;
}

## Slide 14: Test Plan
  Unit tests developed in tandem with module development
  Mock object implementations utilized to:
    Focus testing to individual modules
    Replace dependency on hardware drivers and events
  Hardware drivers to be manually tested (initially) to ensure correctness during development
  SD Card: basic read data tests – output to console
  Web Server: serving simple web pages
  Results to date:
    Core application logic prototyped and passing unit tests
    Verified PCM sample decoding using both MP3 decoding libraries
    SD card functionality and basic I/O such as the LCD, push buttons, and switches

## Slide 15: Questions?