## Slide 1: Step Counter Music DJ
Troy Davis and Caitlin Smart

## Slide 2: Overview
Motivation is to make jogging more fun through music by having the beat of the music match your pace
Read and decode WAV files from SD card
Accelerometer measures x-axis pace
Displays current song and average steps per minute on LCD
Audio plays through speakers

## Slide 3: Hardware
Altera DE2 Development Board with Cyclone II FPGA and Nios-II/f processor
Freescale Semiconductor MMA8452Q Triple Axis Accelerometer
SD Card
Speakers from headphone jack
On-board Wolfson Microelectronics WM8731 Audio Codec

## Slide 4: Hardware Block Diagram

## Slide 5: Hardware Design Considerations
I²C Master bus contention
  Multiple bus masters caused I²C contention within the Quartus design suite
  Adopted isolated component design with the creation of a secondary I²C bus
Accelerometer configuration
  Configured to interrupt Nios II processor when x-axis acceleration exceeds 0.378 g using transient motion settings

## Slide 6: Hardware Design Considerations cont.
Audio codec configuration
  Using the 27 MHz onboard clock we were able to provide the audio codec with input clock frequency of 18.432 MHz which corresponds to an audio sample rate of 48kHz
  Configured audio codec registers using isolated I²C master component in hardware

## Slide 7: Software Block Diagram

## Slide 8: Software Design
Software implementation is broken down into four tasks: main, accelerometer, audio player, and synchronization
Main: initializes data structures and other tasks
Accelerometer: calculates average steps per minute (SPM) based on an average of the last 50 measurements to more accurately model SPM and mask against variances in step rate

## Slide 9: Software Design cont.
Audio player: selects a song from the SD card within a beats per minute (BPM) range that matches the average SPM. The song is played to completion, at which point a new song is selected
Synchronization: pends on button press. When pressed, the current song ends, forcing audio player to select a new song

## Slide 10: Challenges
Interfacing the accelerometer using I²C
  Using two masters (for accelerometer and audio codec)
  Creating a bidirectional tri-state accelerometer component
Decoding MP3 files
Initializing audio codec

## Slide 11: Future Work
Implement MP3 decoding instead of WAV, possibly using MAD lib decoder
Transfer project onto a smaller portable board, such as Altera DE0 nano, which has a built in accelerometer. This board doesn't have a built in audio codec so it would have to be implemented.

## Slide 12: Demonstration
For demo purposes 30 second samples are used on the SD card.
Reference metronome samples are included to demonstrate accuracy.