## Slide 1: Mapping Robot
Group 3: Corey Jamison, Joel Keeling, Mark Langen

## Slide 2: The Problem
  S
  L
  A
  M
  Simultaneous
  Localization
  And
  Mapping
  “Where am I?” (Localization)
  “What does the world look like?” (Mapping)

## Slide 3: Why?
Fundamental problem for autonomous robots’ navigation
  Roomba, Google self-driving car
Alternatives:
  Dead reckoning unreliable
  GPS not accurate enough (4 meter RMS accuracy)
  External sensors – robot only works in prepared areas

## Slide 4: The Project
Two-dimensional SLAM
Robot is manually controlled by a human
Simplify the problem by alternating between movement & scanning

## Slide 5: The Project
Use an accurate LIDAR sensor to measure distance
  PulsedLight’s LIDAR lite unit
Mount it on top of a rotating motor
  Stepper motor
Mount the rotating sensor on a mobile platform
  DFRobot Turtle 2WD platform

## Slide 6: The Project
Two-way communication via Bluetooth with a mobile application (data and commands)
Feed raw data into SLAM algorithm
Display resulting map and position on mobile application, send user’s commands back to robot

## Slide 7: Algorithm Design

## Slide 8: Algorithm Design
After each movement, do a full 360° sweep
Convert array of distance/angle measurements into line segments
  Co-linear points found by linear regression
Compare new line segments to existing map to determine new position & orientation
After adjusting position & orientation, use array of measurements to refine the map

## Slide 9: Algorithm Design
Histogram approach:
  Determine position deltas between new data and old map
  Collect position deltas into histogram
  Choose the peak of the histogram as the true delta
  Similar approach used for rotation

## Slide 10: Hardware Design

## Slide 11: Hardware Benchmarks
LIDAR Lite unit:
  One distance measurement every 20 ms (50 / second)
  Accuracy of ±2cm
  Resolution of 1cm
  Range of ~10cm to ~40m
Stepper motor
  Angular resolution of 1.8° (200 steps for 360° rotation)

## Slide 12: Challenges Overcome
Bluetooth packet loss
  Bi-directional triple redundancy error checking
  Watchdog timer to stop motors
DC motor imbalances
  Doesn’t drive in straight lines
  Algorithm accounts for arcing movements
Found the last LIDAR lite sensor in existence

## Slide 13: Postmortem
What would we do differently?
  More accurate simulations & more iteration time on algorithm
  Better parts – in particular DC motors and chassis ball bearing “wheel”
Future work / extensions:
  Autonomous mapping
  Optimize mapping algorithm to run on board
  Scan while moving

## Slide 14: How to read the map
Black circle: current position
Black line: orientation

## Slide 15: How to read the map
Blue dots: newest LIDAR measurement array

## Slide 16: How to read the map
Grey lines: previously existing line segments

## Slide 17: How to read the map
Red lines: new line segments

## Slide 18: Demo & Questions