## Slide 1: MEC E 265 Engineering graphics and Cad
Lecture XV
Dr. Ahmed Qureshi
Geometric Dimensioning and Tolerancing

## Slide 2: Three Categories of Dimensioning
Dimensioning can be divided into three categories:
  General (size) dimensioning
  Geometric dimensioning
  Surface texture
  The following notes provides information necessary to begin to understand geometric dimensioning and tolerancing
  The note is an outline in nature to provide general guidance. This subject is complex and it is wise to consult the standards and have a clear understanding of what is required when including geometric tolerances on technical drawings.

## Slide 3: Example – a simple shaft
A shaft may be within tolerance as far as the diameter dimension is concerned, but it could be useless if it is not acceptably straight within its length.
Shaft must fit into a hole with a Ø.260 inch mating envelope
Example of a Simple shaft
Linear/angular dimensions and tolerances are used to define part size
Shaft can be lobed or bent but still meet size dimension requirement
There is no form control for “roundness”
There is also no form control for “straightness”

## Slide 4: Example – a simple shaft
All three shafts are subject to Conical, Concave/Convex, and Bending errors
All three cases are acceptable in terms of size dimension requirement, but some parts may not be functional well.
we need geometric tolerancing to define geometry characters, for example, straightness, roundness, etc.

## Slide 5: Geometric Dimensioning & Tolerancing (GD&T)
GD&T is a means of dimensioning & tolerancing a drawing which considers the function of the part and how this part functions with related parts.
  This allows a drawing to contain a more defined feature more accurately, without increasing tolerances.
GD&T is a system (a symbolic language) that uses standard symbols to indicate tolerances that are based on the feature’s geometry.
GD&T practices are specified in
BS ISO 5459:2011 Geometrical product specifications (GPS) — Geometrical tolerancing — Datums and datum systems
BS ISO 1101:2005. Geometrical Product Specifications (GPS) — Geometrical tolerancing — Tolerances of form, orientation, location and run-out

## Slide 6: Without Using GD&T
Given table height
27±1 inch
However, all surfaces have a degree of waviness, or smoothness. For example, the surface of wood is much wavier (rough) than the surface of a piece of glass.
  As the table height is dimensioned, these tables would pass inspection.
If top must be flatter, you could tighten the tolerance to ±0.03. 27±0.03 inch
  However, now the height is restricted to 26.97 to 27.03 meaning good tables would be rejected.
Assume all 4 legs will be cut to length at the same time.
or

## Slide 7: Using GD&T
You can have both, by using GD&T.
  The table height may any height between 26 and 28 inches.
  The table top must be flat within 0.06. (±0.03)
27
.06
26
.06
28
.06
(a)
(b)
(c)
All three cases are acceptable since they’ve met both size and geometric requirement.

## Slide 8: Why is GD&T Important
Saves money and time
  It saves money by providing manufacturing with the maximum functional tolerances.
Ensures design, dimension, and tolerance requirements as they relate to the actual function
Ensures interchangeability of mating parts at the assembly
Provides uniformity – common engineering language, it is a universal understanding of the symbols instead of words

## Slide 9: When to use GD&T
When part features are critical to a function or interchangeability
When functional gauging is desirable
When datum references are desirable to ensure consistency between design, manufacturing and inspection
When standard interpretation or tolerance is not already implied
Note that the indication of geometric tolerances on a drawing should not imply the use of any particular method of production, measurement or gauging.

## Slide 10: Gauging

## Slide 11: Terms used in Geometric Tolerancing
Feature: the general term used to identify part of or a portion of a component., e.g. surface, axis of a cylinder, etc.
Datum is a point, line, plane, or other surface from which dimensions are measured or to which geometric tolerances are referenced.
Maximum Material Condition (MMC): The condition where a size feature contains the maximum amount of material within the stated limits of size. i.e., largest shaft and smallest hole.
Least Material Condition (LMC): The condition where a size feature contains the least amount of material within the stated limits of size. i.e., smallest shaft and largest hole.
Virtual size: the dimension of the overall envelope of perfect form which touches the highest point of a feature
Notes: Just like other written languages have grammar, GD&T as part of engineering drawing language has defined standard.
BS ISO 5459:2011 Geometrical product specifications (GPS) — Geometrical tolerancing — Datums and datum systems
BS ISO 1101:2005. Geometrical Product Specifications (GPS) — Geometrical tolerancing — Tolerances of form, orientation, location and run-out
  MMC for a shaft is the largest allowable size.
    MMC of Ø24 ± 0.5?
  MMC for a hole is the smallest allowable size.
    MMC of Ø25 ± 0.5?

## Slide 12: Symbols for geometric characteristics

## Slide 13: Symbols for geometric characteristics
  Maximum Material Condition MMC
  Least Material Condition LMC
  Diametrical (Cylindrical) Tolerance Zone or Feature
  Datum Feature Symbol
  Feature Control Frame

## Slide 14: Feature Control Frame
Uses feature control frames to indicate tolerance
Reads as: The specified feature must lie perpendicular within a tolerance zone of 0.05 diameter at the maximum material condition, relative to datum axis C.

## Slide 15: Datum
Datums are features (points, axis, and planes) on the object that are used as reference surfaces from which other measurements are made. Used in designing, tooling, manufacturing, inspecting, and assembling.
  not every GD&T feature requires a datum, i.e., Flatness
1.000

## Slide 16: Maximum Material Principle
It recognizes the fact that the allowable errors in geometry of two mating features may be allowed to increase as the size of the features decreases from the maximum material condition (MMC) to the least material condition (LMC).
When the symbol is not used. The allowable geometric tolerance applied regardless of feature size, and no relationship is intended to exist between the feature size and geometric tolerance
When the symbol is included with the geometric tolerance. It means that when the feature is at its maximum material condition an extra geometry tolerance may be allowed.
Notes: This is when part will weigh the most.

## Slide 17: Form Features
Individual Features
No Datum Reference
Flatness
Straightness
Cylindricity
Circularity

## Slide 18: Form Features - Flatness Example
A flatness tolerance is used to control the flatness of a surface.
Flatness as stated on drawing: The flatness of the feature (the surface) must be within 0.02 tolerance zone (i.e. between two parallel planes 0.02 apart).

## Slide 19: Form Features – Straightness Example
A straightness tolerance may be used to control
straightness of a line
straightness of an axis in a single plane
straightness of the axes of solids of revolution
Any actual line on the top surface must lie between two horizontal parallel lines 0.02 mm apart
Any longitudinal line of the surface must lie between two parallel lines 0.02 mm apart
The axis of cylinder A only must lie within a cylindrical tolerance zone of 0.02mm diameter

## Slide 20: Form Features – Straightness at MMC
Meanings:
(a) The maximum diameter of the shaft with perfect form is shown in a gage with a Φ16.04 hole
(b) With the shaft at maximum diameter (16), the gage will accept the shaft with upto 0.04 variation in straightness.
(c) With the shaft at minimum diameter (15.89), the gage will accept the shaft with upto 0.15 variation in straightness.
The derived median line of the feature actual local size must lie within a cylindrical tolerance zone of 0.04 diameter at MMC. As each actual local size departs from MMC, an increase in the diameter tolerance cylinder is allowed which is equal to the amount of such departure

## Slide 21: Form Features – Circularity (Roundness)
A circularity tolerance specifies the width of an annular tolerance zone bounded by two concentric circles in the same plane, within which the circumference of the feature must lie.
Any cross-section of the cylinder perpendicular to the axis must lie between two concentric circles of radial distance 0.25 mm apart

## Slide 22: Form Features – Cylindricity
A cylindricity tolerance specifies a tolerance zone consisting of an annular space between two co-axial cylinders having a difference in radii equal to specified tolerance within which the entire cylindrical surface the feature must lie.
The cylindrical surface of the part must lie between two cylindrical surfaces co-axial with each other and a radial distance of 0.25 mm apart

## Slide 23: Orientation Features - Parallelism
A parallelism tolerance is used to control the orientation of features related to one another by an angle of zero degree. The feature to be controlled may be an axis or a plane surface, and the datum to which it is orientated may also be axis or a plane surface.
The surface of the part must lie between two parallel planes 0.12 mm apart which are parallel to datum plane A.

## Slide 24: Orientation Features - Parallelism
A parallelism tolerance is used to control the orientation of features related to one another by an angle of zero degree. The feature to be controlled may be an axis or a plane surface, and the datum to which it is orientated may also be axis or a plane surface.
The axis of the top hole must lie inside a cylindrical tolerance zone 0.2 mm diameter which has its axis parallel to the other hole axis, datum A
Notes: .

## Slide 25: Location Features - Concentricity
A concentricity tolerance is used to control a condition in which two or more features such as circles, spheres, cylinders, cones or hexagons are required to share a common centre or axis.
The axis of the right-hand end of the shaft must lie within a cylinder 0.06 diameter, which is co-axis with datum A, the axis of the left hand end of the shaft.
The axis of the left-hand and right-hand cylinder ends of the shaft must lie within a cylinder 0.06 diameter

## Slide 26: Location Features - Position
A position tolerance is used to control the location of a feature by limiting its deviation from a specified true position
The axis of each hole must be contained within a cylinder 0.05 diameter through the thickness of the material. Each axis being in its true position in relation to the datum plane A and datum hole B

## Slide 27: Analysis of geometric tolerances

## Slide 28: Analysis of geometric tolerances

## Slide 29: Summary
Dimensional tolerances control size and geometric tolerances control shape and position.
GD&T should be used to refine the relationship between feature and form.
GD&T should open tolerances. MMC should reduce part cost.
It is not necessary to use geometric tolerances for every feature on a part drawing.

## Slide 30: Reference Standards
BS ISO 1101:2005 Technical Drawings - Geometrical tolerancing - Tolerancing of form, orientation, location and run-out - Generalities, definitions, symbols, indications on drawings.
BS ISO 5459: 2011 Technical Drawings - Geometrical tolerancing - Datums and datum-systems for geometrical tolerances.