## Geophysics 224 Mid-term exam		Name:___________________

Instructor		Dr. Martyn Unsworth

Date			Wednesday February 16th 2005

Time allowed		2:00 p.m. to 3:20 p.m.

Total = 68 points

Please attempt ALL questions

Notes and books may NOT  be used during the exam

Calculators are permitted

Please show all working, as credit will be given for method as well as the final answer

All questions should be directed to the invigilator

Please hand in this exam, with your answer booklet

#### Question 1  (Total 20 points)

A shot (S1) was fired at the surface at time t=0 and a seismic signal was generated with amplitude, A=1.

- Compute the arrival time and amplitude for the first three reflections arrivals to reach  the geophone (R1).														(12 points)

- Sketch the seismic traces recorded at R1.

Show the amplitude and sign of each reflection		(4 points)

- The velocity of the gas is 300 m/s

The velocity of the sandstone matrix is 3000 m/s.

Calculate the porosity of the gas reservoir? 		(4 points)

Question 2  (Total 20 points)

Weapons inspectors are looking for a buried cylindrical tunnel. The tunnel was located beneath an alluvium filled river channel. Densities in this area were:

Density of air in tunnel      	=  0 kg m-3

Bedrock density   		=  2200 kg m-3

Alluvium density 		=  1900 kg m-3

Microgravity data were collected on the profile shown below.

- How thick is the alluvium in the  river channel?			(5 points)

- What is the depth of the centre of the tunnel?			(6 points)

- Is the tunnel located in the alluvium or bedrock?			(2 points)

- What is the radius of the tunnel? 				(6 points)

x(m)     g (mgals)

10.        -0.0004

20.        -0.0005

30.        -0.0006

40.        -0.0007

50.        -0.0260

60.        -0.0262

70.        -0.0264

80.        -0.0268

100.        -0.0283

110.        -0.0300

114.        -0.0311

116.        -0.0318

118.        -0.0325

120.        -0.0334

122.        -0.0345

124.        -0.0358

x(m)       g (mgals)

126.         -0.0374

128.         -0.0394

130.         -0.0417

132.         -0.0447

134.         -0.0485

136.         -0.0532

138.         -0.0592

140.         -0.0670

142.         -0.0757

144.         -0.0862

146.         -0.0967

148.         -0.1049

150.         -0.1081

152.         -0.1049

154.         -0.0967

160.         -0.0670

Question 3  (Total 28 points)

- What three factors that cause the acceleration of gravity to vary from the North Pole to the Equator?

For each, make it clear if gravity is stronger at the North Pole or Equator

(6 points)

- Outline how the Vibroseis method works.

Explain the main differences between Vibroseis surveys

and seismic surveys using explosives.				(6 points)

- Explain what is meant by non-uniqueness in geophysics?

Using a figure, give an example from gravity exploration

(6 points)

- Why are high frequency seismic signals attenuated more rapidly than low frequency signals?							(4 points)

- In what two ways is the Bouguer correction approximate?

(2 points)

- Why can’t gravity be measured in a satellite using conventional gravimeters?

How  is “satellite gravity” actually measured?

(4 points)

Formulae that may be useful

B :  Gravity exploration

a   = radius of sphere or cylinder		Δρ = density contrast

z    = depth of the sphere or cylinder		x = horizontal distance from sphere/cylinder

G   = 6.67 x 10-11 N m2 kg-2			1 milligal 	= 10-5 ms-2

MS = excess mass				x½		= half width

Cylinder  		x½   = z

Sphere 			x½  = 0.766z

Gravitational attraction of slab with thickness Δh (m) and density contrast Δ ρ (kg m-3)

Δgz = 2πGΔh Δ ρ  (ms-2)

Change in gz when elevation changes by Δz (m)		Δgz = 0.3 Δz (milligals)

C : Seismic exploration

v = velocity;	t = travel time;		x = source-receiver offset;	ρ = density;

v = distance

time

For a porous rock, the velocity (v) is given by the time average equation:

where  Φ = porosity; vf = velocity in fluid; vm = velocity in rock matrix

Seismic impedance , Z = ρv

Seismic wave travelling from layer 1 to layer 2, at normal incidence

Amplitude reflection coefficient,      R =

Amplitude transmission coefficient, T =

Normal moveout (NMO)  =  where  t1 = travel time at normal incidence

Travel time for a reflection,